## Slide 1
4
MODULE 4
Spatio-Temporal Bottleneck Forecasting &
Dynamic Carrying Capacity
Forecasts where and when trail sections overload, a day ahead, from open data only - and turns it into a safe number per trail instead of one fixed daily quota.
Your photo
(keep the one in the team deck)
CONTRIBUTION TO THE OVERALL SOLUTION
Supplies the crowd and capacity signal of the framework: a per-section forecast and safe numbers that the safety assistant (Module 3) and the authority dashboard read offline through a versioned data contract.
SPECIALIZATION Information Technology
IT23343948 | Weerasekera J.V | J26-IT-363

## Slide 2
MODULE 4 · CROWD & CAPACITY FORECASTING
How the solution addresses the sub-problem / prototype
Working prototype at three parks (Horton Plains, Adam's Peak, Yala). Results: 2025 replay, simulation.
SUB-PROBLEM
One fixed daily quota per park cannot say when or where a trail section overloads - and no section counts exist.
USER REQUIREMENTS MET
✓ Section-level forecast, next 24 h (FR2)
✓ Condition-aware capacity, Cifuentes (FR3)
✓ Runs offline on the phone < 2 s (NFR1)
✓ One number + 'why' for officials (NFR4)
✓ Feed for Module 3 + dashboard (FR4)
✓ Tested against simple baselines
PROTOTYPE FLOW
OpenStreetMap trail graph
35-57 sections of ~300 m - 1.2 km
Terrain + weather + calendar
Copernicus DEM, Open-Meteo, Poya days
ST-GNN: GCN + GRU
people per section per hour, on the phone
Cifuentes PCC → RCC → ECC
forecast enters the real-capacity step
Decisions
safe numbers · entry slots · gate advice
Tomorrow, section by section (offline)
Officer: forecast vs fixed quota
−27%
over-capacity vs fixed quota (Horton)
−24%
same, at Adam's Peak
−99.6%
with timed entry slots
<2 s
forecast on the phone
Same visitors admitted in every comparison. Slot tickets fix a trail + entry time, so no section goes over its safe number in any half hour.
16

## Slide 3
MODULE 4 · CROWD & CAPACITY FORECASTING
Design excellence / contribution + user feedback
Tested, not assumed: the graph model is compared with simpler models, and the parts that did not work are reported.
Graph structure
Tiny trail graphs (35-57 sections) built from OpenStreetMap - not dense city traffic. One config file per park: Horton Plains, Adam's Peak, Yala.
Transfer strategy
Pretrained on METR-LA → PEMS-BAY, adapted to each trail. Honest result: helps only with 30-90 days of data; traffic weights alone fail.
Management value
Forecast enters Cifuentes RCC → a safe number per trail that changes with weather and crowding: −27% / −24% over-capacity time vs a fixed quota.
Validation · baseline comparison
MAE (people / section-hour) | Hist. avg | ARIMA | LSTM | GRU, no graph | ST-GNN
Every section counted | 1.60 | 1.93 | 1.42 | 1.42 | 1.42
Sections without counts | 4.20 | – | 2.59 | 2.61 | 2.54
Horton Plains, 2025 test year, 3 seeds, paired tests over days. Graph helps on uncounted sections (p < 0.001, ~2 %); a tie when every section is counted. Spatial block CV; no leakage.
Day-ahead forecast vs actual at World's End: right on typical days, low on the rare busiest day → decisions use the busy case.
USER FEEDBACK
Fill with real answers before presenting:
• Hiker: would you change your visit if a section shows red at 08:00?
• Guide / tour operator: is the safe number + reason clear?
• Ranger / DWC contact: would the counting + gate advice fit the job?
• Changed because of it: …
Next Field counts in December (criteria fixed in advance) to validate the simulated target; surveys with DWC, rangers and hikers.
17